## Slide 1
Introduction to Computer Science
Shimon Schocken
IDC Herzliya
Lecture 7-2
Computer Fundamentals
Part I
Notes: 1

## Slide 2: Overview
Goals
Explore how computers work
Explore low-level programming
Explore the road from the low-level to the high level
Approach
Introduce a simple hardware platform
Write some machine language programs
Understand the hardware – software interplay, hands-on.
computer

## Slide 3: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 4: Vic: a simple computer architecture (www1.idc.ac.il/vic)
0
1

## Slide 5: Vic: a simple computer architecture (www1.idc.ac.il/vic)
read
write
load
store
add
sub
...
instructions:
inside view:
outside view:
can I make this thing do some useful things?
Hmmm … How

## Slide 6: Data bus
write to output
read from input
store to memory
load from memory
0
1

## Slide 7: Instruction set
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 8: Read operation
following execution:
read
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 9: Write operation
following execution:
write
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 10: Load operation
load 90
following execution:
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 11: Store operation
store 91
following execution:
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 12: Add operation
add 87
following execution:
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 13: Subtract operation
sub 85
following execution:
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]

## Slide 14: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 15: Low-level programming
Task: read two numbers and write their sum.
High-level programming:
Think about the code abstractly, using a formalism like Java / Python,
Without worrying about how the machine handles this logic.
Logic / algorithm
x = read a number
y = read a number
print(x + y)
High-level thinking…

## Slide 16: Low-level programming
Task: read two numbers and write their sum.
read a number
store it somewhere // a
read a number
store it somewhere // b
add a // to D
write
stop
Logic / algorithm
00
01
02
03
04
05
06
read
store 90
read
store 91
add 90
write
stop
symbolic program
implement
00
01
02
03
04
05
06
executable code
800
490
800
491
190
900
000
translate
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]
Low-level programming:
Thinking about the code mechanically, in terms of machine-level operations.
Low-level thinking…

## Slide 17: Loading and executing a program
Loaded ”read and add two numbers" code
after the program terminates:
execute

## Slide 18: Loading and executing a program
When I load a program into the computer and say “execute”, the program gets executed
How does this magic happen?
How is the fetch-execute logic implemented?
It is hard-wired into the computer hardware (not shown in this lecture).
PC:
IR:
D:
Fetch-execute cycle:
(basic version)
PC = 0
fetch:
IR = M[PC]
if (IR == 0) goto end
execute IR (read, write, load, …)
PC++
goto fetch
end:
do nothing

## Slide 19: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 20: Branching
command
command
command
command
command
command
command
command
command
command
command
command
command
command
Default flow of control: linear
command
label a
command
if condition goto b
command
command
label b
command
command
if condition goto c
command
label c
command
goto a
Typical flow of control: branching

## Slide 21: Branching
Low-level branching instruction: goto addr
addr: An address, marks a location in the code
goto: Used to transfer the flow of control to a selected location in the code
Task (example): Read and write until 0 is read
00
01
02
03
04
read
gotoz 04
write
goto 00
stop
Vic features three branching instructions:
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics

## Slide 22: Branching
Task: Read two numbers and write the greater one
machine language
00
01
02
03
04
05
06
07
08
09
10
11
...
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
Branching instructions:

## Slide 23: Branching
Task: Read two numbers and write the greater one
machine language
00
01
02
03
04
05
06
07
08
09
10
11
...
read
store x
read
store y
sub x
gotop YISMAX
load x
write
stop
load y
write
stop
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
Branching instructions:

## Slide 24: Branching
Task: Read two numbers and write the greater one
machine language
read
store x
read
store y
sub x
gotop YISMAX
load x
write
stop
load y
write
stop
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
Branching instructions:
00
01
02
03
04
05
06
07
08
09
10
11
...

## Slide 25: Branching
Task: Read two numbers and write the greater one
machine language
read
store x
read
store y
sub x
gotop 09
load x
write
stop
load y
write
stop
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
Branching instructions:
00
01
02
03
04
05
06
07
08
09
10
11
...

## Slide 26: Branching
Task: Read two numbers and write the greater one
machine language
read
store x
read
store y
sub x
gotop 09
load x
write
stop
load y
write
stop
executable code
translate
00
01
02
03
04
05
06
07
08
09
10
11
...
800
490
800
491
290
709
390
900
000
391
900
000
Convention: Allocate variables to memory, from address 90 onward:
x: represented by M[90]
y: represented by M[91]
load
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
Branching instructions:
00
01
02
03
04
05
06
07
08
09
10
11
...

## Slide 27: Branching
“max of two numbers” program
After the program terminates:

## Slide 28: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 29: Fetch–execute cycle
PC = 0
fetch:
IR == M[PC]
if (IR == 0) goto end
if ( (IR == 5xx) or
(IR == 6xx and D == 0) or
(IR == 7xx and D > 0) )
PC = xx
else
execute IR (read, write, load, store, add, sub)
PC++
goto fetch
end:
goto end
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx
Symbolic Exec. Semantics
PC:
IR:
D:

## Slide 30: Fetch–execute cycle
That’s it! the description of the Vic computer is now complete.
PC:
IR:
D:
PC = 0
fetch:
IR == M[PC]
if (IR == 0) goto end
if ( (IR == 5xx) or
(IR == 6xx and D == 0) or
(IR == 7xx and D > 0) )
PC = xx
else
execute IR (read, write, load, store, add, sub)
PC++
goto fetch
end:
goto end

## Slide 31: The Vic computer specification (recap)
Conventions:
each command is represented as a 3-digit number
D: data register
xx: a two digit number
M[xx]: contents of the RAM at address xx
I/O
Instructions
memory Instructions
arithmetic Instructions
control Instructions
RAM
CPU
I/O
symbolic numeric semantics
syntax syntax (meaning)
read 800 D = input
write 900 output = D
load xx 3xx D = M[xx]
store xx 4xx M[xx] = D
add xx 1xx D = D + M[xx]
sub xx 2xx D = D - M[xx]
goto xx 5xx goto xx
gotoz xx 6xx if (D == 0) goto xx
gotop xx 7xx if (D > 0) goto xx

## Slide 32: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 33: Symbolic programming
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
Express the pseudo code using machine instructions
write
Symbolic Exec. Semantics
Instruction set

## Slide 34: Symbolic programming
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
// sum = 0
load zero
store sum
LOOP:
// read x
read
store x
// if (x == 0) goto END
gotoz END
// sum = sum + x
load sum
add x
store sum
goto LOOP
END:
// write sum
load sum
write
stop
Symbolic program
Express the pseudo code using machine instructions
write
Symbolic Exec. Semantics
Instruction set
Let’s remove the white space, and add line numbers

## Slide 35: Symbolic programming
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
00
01
02
03
04
05
06
07
08
09
10
11
Instruction set
write

## Slide 36: Program translation
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
00
01
02
03
04
05
06
07
08
09
10
11
Instruction set
write
Symbol table:
zero: 98
one: 99
sum: 90
x: 91
LOOP: 2
END: 9
Symbol table:
Maps every symbol in the program to a memory address

## Slide 37: Program translation
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
00
01
02
03
04
05
06
07
08
09
10
11
translate
Executable code
398
490
800
491
609
390
191
490
502
390
900
000
00
01
02
03
04
05
06
07
08
09
10
11
Symbol table:
zero: 98
one: 99
sum: 90
x: 91
LOOP: 2
END: 9
Instruction set
Symbol table:
Maps every symbol in the program to a memory address
write

## Slide 38: Program translation
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
00
01
02
03
04
05
06
07
08
09
10
11
translate
Executable code
398
490
800
491
609
390
191
490
502
390
900
000
00
01
02
03
04
05
06
07
08
09
10
11
Symbol table:
zero: 98
one: 99
sum: 90
x: 91
LOOP: 2
END: 9
Observations
Compared to executable code, symbolic code is much easier to write / debug / maintain.
The symbolic code mentions no physical addresses. Therefore, it is relocatable.
The translation process can be automated.
write

## Slide 39: Program translation
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Symbolic program
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
00
01
02
03
04
05
06
07
08
09
10
11
translate
Executable code
398
490
800
491
609
390
191
490
502
390
900
000
00
01
02
03
04
05
06
07
08
09
10
11
Symbol table:
zero: 98
one: 99
sum: 90
x: 91
LOOP: 2
END: 9
Terminology
Symbolic low-level code is called “assembly code”
The translator program is called “assembler”
write

## Slide 40: Program translation: Vic
Pseudo code (goto-oriented)
sum = 0
LOOP:
read x
if (x == 0) goto END
sum = sum + x
goto LOOP
END:
write sum
stop
Task: sum up a series of numbers that ends with a zero
Sum.asm
load zero
store sum
LOOP:
read
store x
gotoz END
load sum
add x
store sum
goto LOOP
END:
load sum
write
stop
translate
Sum.vic
398
490
800
491
609
390
191
490
502
390
900
000
write
Using a text editor,
you write a Vic assembly program
Using the Vic Assembler,
you translate the assembly code into executable code

## Slide 41: The Vic assembler
Loads an .asm file
1
2
Loads the resulting .vic file into the Vic computer
3
Task: sum up a series of numbers that ends with a zero

## Slide 42: Executing the translated code
Task: sum up a series of numbers that ends with a zero
Enter some test data
Loaded code

## Slide 43: Executing the translated code
Task: sum up a series of numbers that ends with a zero
Enter some test data
Loaded code
result

## Slide 44: Lecture plan
Hardware platform (Vic)
    Architecture
    Instructions
Low-level programming
    Basic
    Branching
Fetch-execute cycle
Program translation
From Vic to a real computer

## Slide 45: From Vic to the real thing
Suppose we have unlimited supplies of money, time, and creativity;
How can we evolve Vic into a real computer?

## Slide 46: From Vic to a real computer system: Hardware
Vic: Typical PC:
1 data register ……………… 32 data registers
3-digit words ....................... 64-bit words
100 memory cells ………….. billions of memory cells
1 memory unit ……………… RAM, ROM, cache
No secondary storage ………. disk
1 input port ………………… keyboard, mouse, disk, modem, …
1 output port………………… screen, speakers, disk, network, …
1 “computer”……………….. CPU + various I/O processors, one for each I/O device
10 Instructions ……………... 100-300 Instructions
1 program …………………. several programs running “simultaneously”
1 instruction per cycle …….. parallel processing.
RAM
CPU
I/O
Implementing any one of these improvements is a straightforward extension of the basic Vic architecture.

## Slide 47: Hardware architecture
Intel CPU
Qualcom CPU
ARM CPU
Almost all modern computers are variations of this basic model:
Vic CPU
. . .

## Slide 48: Hardware architecture

## Slide 49: Hardware architecture
processor
hard disks
memory stick
screen
speakers
printer
keyboard
scanner
mouse
main memory
Cache
memory
external
storage
network
interface
card
network
backbone
I/O devices
processing
devices
bus
processor
processors
processing
devices
system programs
unused area
app2
app1
app3
unused area
file 2 (paged)
file 3 (paged)
unused area
file 1 (paged)

## Slide 50: Hardware architecture
Thanks goodness for abstractions!
Computer Science (CS): Focus on logical operations
Electrical engineering (EE): Focuses on physical implementations

## Slide 51: A peek into a real machine language
It’s important to remember that Vic is a simple metaphor

## Slide 52: A peek into a real machine language
C program, typical 2D array processing

## Slide 53: A peek into a real machine language
Shows the compiled code generated by a C compiler:
1: RAM address (in hexa)
2: Binary instructions (32-bit, in hexa)
3: Symbolic instructions (op code, followed by parameters)
1
2
3
Tranlsated to RISCV, a 47-instruction set, used in many modern CPUs

## Slide 54
Introduction to Computer Science
Shimon Schocken
IDC Herzliya
Lecture 7-2
Computer Fundamentals
Part I
Notes: 54